## Slide 1
Balancing Glare and Circadian Stimulus
with Shade Fabric Simulation
Ka Kit Chiu
University of Washington CBE
Thesis Advisor: Mehlika Inanici
Committee Member: Christopher Meek
image credit: Yuan 2022
Notes: Good morning everyone. My name is Ka Kit Chiu, thank you for coming to the presentation of my thesis, titled “Balancing Glare and Circadian Stimulus
with Shade Fabric Simulation”. This research is conducted at UW under the guidance of my thesis advisor Mehlika Inanici, and committee member Christopher Meek. In this research, we have been exploring how shade fabric can be manipulated to enhance both visual comfort and circadian health.

## Slide 2
Content
Research Problem (Glare vs Circadian Stimulus)
Background
  Circadian Rhythm
  Human Ocular System
Glare and Circadian Metrics
Simulation Method
  Parameters
  Shade Fabric Materials
Result
  Comparison of available products with proposed spectrally selective shade fabric alternatives
Conclusion
Notes: Here is a quick structure of this presentation, starting with the research problem of balancing glare and circadian Stimulus, we will explore the background covering the relationship between our circadian rhythm and human ocular system. Next, we'll discuss the metrics used to evaluate glare and circadian effects, followed by the simulation methods, including parameters and shade fabric materials. The results will compare available products with proposed spectrally selective shade fabric alternatives. Finally, we'll summarize the findings and conclude with key takeaways."

## Slide 3
When we encounter glare…
We often use shade fabrics for glare controls but…
It reduces light penetration to deeper space
It reduces the circadian stimulus and disrupts our circadian rhythm
Image: Ka Kit Chiu
Notes: When we encounter glare, we often deploy shade fabrics to control the glare issue. However, while these fabrics are effective, they also reduce light penetration into deeper spaces and diminish the circadian stimulus, thereby disrupting our natural circadian rhythm.

## Slide 4
Regulate and coordinate body functions over 24 hours
23.7 – 25.1 hrs (Lockley 2009)
Synchronization requires:
  Light intensity
  Duration
  Correct Timing
  Wavelength / Color
Circadian Rhythm
Image: Elenabsl / Shutterstock.com
Notes: So what is CR, and why is it important? Our circadian rhythm regulates and coordinates our body's functions over a 24-hour period, such as melatonin secretion, body temperature, blood pressure, and alertness… etc. And previous studies have found out some people may have shorter “Circadian Clock”, and some may have long CR. And we need specific condition of lights to help our bodies synchronized, including the right light intensity, duration, correct timing, and wavelength or color of light.

## Slide 5
Vast natural horizon
Blue sky
Green landscape
Daily cycle of light and dark
Environment: Past vs Now
Indoor environment
Electric lights (since 19th century)
Windowless/ Filtered/ Shaded
Irregular use of light
Notes: In the past, our environment featured vast natural horizons, blue skies, green landscapes, and a consistent daily cycle of light and dark. This natural lighting supported our circadian rhythms and overall well-being. However, our current indoor environments, illuminated by electric lights since the 19th century, often lack windows or have filtered and shaded light. This shift to irregular use of light disrupts our natural cycles to support our circadian health. Here is an example of the SPD of these environment for comparison, daylight provides a broad, continuous spectrum that changes with time of day, supporting our circadian rhythms. In contrast, electirc lights like fluorescent, cool white LED, and incandescent bulbs have narrow, often spiky spectrums that lack the full range of wavelengths found in natural light. This difference in spectral quality is what leads to circadian disruption.

## Slide 6
Current Situation
d
Human spend 90+% of time indoor
  Windowless
  Electric light dominant
AIA Architecture 2030s Vision
  Prioritize building performance
Klepeis, N.; Nelson, W.; Ott, W.; Robinson, J.; Tsang, A.; Switzer, P., et al. (2001). The National Human Activity Pattern Survey (NHAPS): A resource for assessing exposure to environmental pollutants. Journal of Exposure Analysis and Environmental Epidemiology, 11(3). LBNL Report #: LBNL-47713. Retrieved from https://escholarship.org/uc/item/1zg3q68x
Biological Darkness
How can we resolve it?
Notes: Especially nowadays we are spending 90% of our time indoor, it means we are experiencing biological darkness. To address this issue, first we need to understand how our ocular systems works. There’re 2 pathways both are sensitive to different spectrum of light.

## Slide 7
Image Forming Pathways
(Provencio, 2000; Gooley et al., 2001;Hannibal et al., 2002; Hattar, 2002)
4 Photoreceptors:
  Short-wavelength cones (Blue)
  Medium-wavelength cones (Green)
  Long-wavelength cones (Red)
  Rods
Responsible for to color and day/night vision
Notes: The first one is the Image-Forming Pathways, which is responsible for our color/day/night vision. It relies on 4 photoreceptors S-cones, M-cones, L-cones, and Rods.

## Slide 8
Non-Image Forming Pathways
(Provencio, 2000; Gooley et al., 2001;Hannibal et al., 2002; Hattar, 2002)
The 5th photoreceptor:
  Intrinsically photosensitive Retinal Ganglion Cells (ipRGCs)
Suprachiasmatic Nucleus (SCN)
  Adjust circadian clock
  Melanopsin (OPN4) – peaks at 480 nm (Blue light)
  Neuropsin (OPN5) – peaks at 380 nm (UV-Violet light)
Respond to dynamic, stable, light changes
Notes: The 2nd pathways is called the Non-image forming pathways. It relies on the 5th type of photoreceptors known as the intrinsically photosensitive Retinal Ganglion cells (ipRGCs). These cells directly influence our circadian rhythms through the Suprachiasmatic Nucleus (SCN) . And respond primarily to blue light, because it contains melanopsin with sensitivity peaking at 480 nm and neuropsin at 380 nm. That why the blue spectrum of the light has direct impact to synchronizing circadian clock of our bodies.

## Slide 9
By designing the shade fabric based on the photopic and melanopic responsivity, we may be able to achieve a balance between glare and circadian stimulus.
Minimize visual discomfort and maximize circadian stimulus.
Develop a better color scheme that differentiates the melanopic and photopic effect of shading.
Compare shades and venetian blinds.
Objective: Spectrally-Selective Fabric
Notes: As a result, the objective of this research is to design shade fabric to balance glare and circadian stimulus based on the photopic and melanopic responsivity. 1st, we want to minimize visual discomfort and maximize circadian stimulus. 2nd, we want to develop a better color scheme that differentiates the melanopic and photopic effect of shading. 3rd , we also want to compare those effect between shades and venetian

## Slide 10
Photopic (Green: 67%)
Melanopic (Blue: 61%)
Baseline (No Shade)
500nm
588nm
Photopic: 6%
Melanopic: 61%
Photopic: 67%
Melanopic: 39%
Photopic: 26 %
Melanopic: 0.3%
Notes: Here is a visualization on a conceptual level. The graph here presents a baseline condition how we receive light without any shading. 1st, we have the photopic curve with the green area concentrated at the green spectrum, contributing to 67% of our visual sensation. The 2nd one is the Melanopic curve with the blue area concentrated at the blue spectrum contributing to 61% of our circadian entrainment.

## Slide 11
Glare mitigated
Shade Deployed
Circadian light suppressed
Photopic: 6%
Melanopic: 61%
Photopic: 67%
Melanopic: 39%
Photopic: 26 %
Melanopic: 0.3%
500nm
588nm
Notes: This is what happened when we deploy shade fabrics which we mitigate glare by suppressing the excessive light, but at the same time we also suppress circadian light we need for entrainment.

## Slide 12
Proposed Solution
Circadian light regained
Glare mitigated
500nm
588nm
Photopic: 6%
Melanopic: 61%
Photopic: 67%
Melanopic: 39%
Photopic: 26 %
Melanopic: 0.3%
Notes: Since we can see that photopic and Melanopic sensitivities peak at different wavelength of light, we want to preserve as much blue light as possible for circadian entrainment while suppressing enough green light for glare control.

## Slide 13
Light Intensity (300lx – 2657lx)
  Office task: 300lx* (on the table)
  Glare: 2657lx* (Ev at the eye)
WELL v2 L03 Circadian Standard
  Equivalent Melanopic Lux (EML) (Ev at the eye)
  >275EML for 4 hour
Ideal Condition: >275 EML - <2657lx
Glare and Circadian Metrics
image credit: WELL v2 Circadian Light Standard
Wienold J and Christofferson J. “Evaluation methods and development of a new glare prediction model for daylight environments with the use of CCD cameras” Energy and Buildings, 38, 2006
image credit: Classrooms | Thorlux Lighting
Notes: And there are 2 metrics to help us understand where the balance is. An office task generally requires at least 300lx on the table illuminance on horizontal plane, and 2657lx on the vertical plane at eye level is the threshold where we experience glare. Apart from this, the circadian lighting design guideline in chapter L03 of WELL v2 standard has mentioned at least 275 EML for 4 hours in the morning time, which stands for Equivalent Melanopic Lux, a metrics used to quantify the effect of light on the human circadian system, and there is “too much” EML but we propose an upper threshold of 1100EML which required duration can be shortened to 1 hour. Overall, we can summarize it into 5 conditions, “glare” in red, “ideal” in green, “fair” in yellow means lacking EML, “dim” in blue means lacking photopic light, and underlit in grey.

## Slide 14
Simplified DGP:
DGPs = 5.87 x 10-5 x Ev + 0.16
Glare : Daylight Glare Probability (DGP)
Wienold J and Christofferson J. “Evaluation methods and development of a new glare prediction model for daylight environments with the use of CCD cameras” Energy and Buildings, 38, 2006
Imperceptible Glare: Ev < 2657 Lx
Noticeable Glare: Ev 2657 – 3339 Lx
Disturbing Glare: Ev 3339 – 4532 Lx
Intolerable Glare: Ev > 4532 Lx
Ev = 13900 Lx saturates (DGP = 1.0)
Notes: Here is the reason determines why 2657Lx becomes glare. It comes from a formula called Daylight Glare Probability (DGP). It is a metric used to evaluate the likelihood of experiencing glare for daylight in an interior environment. It consists of 2 major parts. The 1st part is the light coming from the surrounding. The 2nd part is our glare sensation from contrast between glare source and its surrounding (such as reflection on our monitor). As our research focuses on the glare from daylight, we can remove the contrast component and use the simplified version of DGP. Referencing the degree of glare scale by Wienold, 0.34 is the threshold of “imperceptible” glare that we plug in the equation to find out this glare value of “2657lx”.
Detail: 0.16 is an empirical value added to better align the theoretical model with observed data form glare studies. (baseline adjustment + calibration)

## Slide 15
A simplified way to describe the color of a light source
Blackbody’s color in different temperature (Unit: Kelvin (K))
Warm (2500K) – Cool (25000+K)
Correlated Color Temperature (CCT)
xy Chromaticity Space (CIE 1931)
image credit: (Hernandez-Andreas, et al 2001)
S/M/L Cones Sensitivities
image credit: The Retrofit Companies, Inc.
Notes: Other than glare and circadian metrics, we also need to understand the sky colors as light source for simulation, Correlated Color Temperature CCT is a simplified way to describe the color of a light source (in this case it is our sky) in terms of color temperature, measured in Kelvin. The sky CCT can range from a warm tone of 2500K to cool tone of over 25000K.

## Slide 16
SPD of eye-level HDR image in Seattle (Jung, Inanici 2018)
image credit: Hernandez-Andreas, et al 2001
CCT of Skies
image credit: Inanici 2022
Affected by weather, seasons, time, view orientations… etc.
CIE standard [D65] = 6500K
Notes: International Commission on Illumination (CIE) positions 6500K as the average daylight CCT throughout the day but it is overly simplified because skies CCT can be influenced by various factors, such as weather, seasons, and even view orientations of the same time. The CCT range should be covered properly in a simulation for more accurate insights and future analysis.

## Slide 17
What is Shade Fabric (SF)?
Transmission (Ts)
  Tv-direct and Tv-diffuse
Absorption (As)
Reflection (Rs)
Openness Factor (OF: 1% - 3% - 5% - 10%) (impact Tv-direct)
Color (impact Tv-diffuse and Rs)
  Lighter color reflect radiation (less glare control)
  Darker color absorb radiation (more heat absorption)
  Standard Color: Grey
image credit: Glare protection fabrics | Roller Blinds (hunterdouglasarchitectural.eu)
image credit: EN 14501 Standard
Notes: Now that we have some understandings of light source, let’s move on to how shade fabric interact with daylight. In short there are 3 types of interaction. 1st, is transmission, meaning a direction light penetration thro fabric. 2nd is Absorption, meaning radiation being absorption by the fabric. 3rd is reflection, meaning light reflected by the fabric. Something worth notices is that Transmission and Reflection both have specular and diffused interactions. Commercial typical products have openness factors (1%,3%,5%,10%) that affect specular transmissions. And the Color of fabrics to control the diffused transmission and all reflections. Light color reflects radiation and have less glare control, while darker color absorb radiation and absorb more heat. Hence, Grey becomes the norm as middle ground.

## Slide 18
1% , 3%, 5%, 10%
Commercial Typical:
Trans (.rad)
BRTDfunc (.rad)
Notes: To simulate the materials, we first look at the solar optical properties and compute those value with a light simulation engine called Radiance developed by Lawrence Berkeley National Lab (LBNL). In Radiance, we have compared 2 material calculations: Trans. Material and BRTDfunc (stands for Bidirectional Reflectance Transmittance Distribution Function). After a quick test we decide to go with BRTDfunc as it provides a more accurate simulation to human visual perception.

## Slide 19
Simulation Method: LARK 3.0 (Multi-spectral lighting)
×
Light source
Material properties
Photopic Lux
=
OPN-1
×
9-Channel Simulation
OPN-4
=
EML
Notes: Overall, this is how the simulation process works. First, we have our light source multiplying with the materials in 9 channels, Lark Spectral Lighting 3.0. Then we further multiply the values with photopic and Melanopic sensitivity curves to find out the amount of photopic lux and EML.

## Slide 20
Platform: Lark 3.0 (9-Channel) in Rhino3D
Classroom: 30’x 30’
Location: Seattle, WA
South Facing Window: 40% WWR
Sitting eye level: 44”
Weather: Clear Sky
Sky CCT: 5500K, 6500K, 13000K, 25000K
Season:
  Sunny Summer (June 21st, 9:00am to 12:00pm)
  Sunny Winter (Dec 21st, 9:00am to 12:00pm)
4 gaze orientations: (N,E,S,W)
Research Setting
image credit: Inanici 2022
Notes: Here are the parameters for the simulation. 1st, we use LARK 3.0 in Rhino3D as the platform. In Rhino3D, a 30’ x 30’ classroom is created (typical class size for 20-25 students in American standard.) It locates in Seattle, WA, with a south facing window of 40% WWR. Simulation takes place at our sitting eye level which is typically 44” from the ground. The weather is set to be Clear sky with varying CCT from 5500K to 25000K because we are tackling glare from natural daylight. Higher CCT value incorporates blueish light whereas lower CCT values incorporate yellowish light. It also focus on summer and winter solstices, across 4 gaze orientation N,E,S,W.

## Slide 21
S
E
N
Notes: Here is the process of the lighting analysis. We 1st look at the light distribution via a grid simulation and then follow up with a section to see the light penetration, and a render to understand how it looks like in human eyes.

## Slide 22
Baseline (No Shade Fabric)
Location: Seattle, WA
Climate: Clear Sky
CCT: 6500K
Jun 21st : 12:00pm
Sitting Eye-level: 44”
Photopic Lx:
EML:
Baseline: No Shade Fabric
Notes: 1st let look at the result for baseline condition.

## Slide 23
Baseline : Jun 21st 12:00pm – OPN 1 vs OPN 4
OPN 1
OPN 4
IDEAL: 55.3%
IDEAL: 71.4%
IDEAL: 48.49%
IDEAL: 58.9%
IDEAL: 55.3%
IDEAL: 71.4%
IDEAL: 48.49%
IDEAL: 58.9%
Notes: Here is the photopic and Melanopic light condition on Summer solstice. After overlap these 2 information together, we

## Slide 25
Summer Jun 21st 12 :00pm
Winter Dec 21st 12 :00pm
Baseline : Balance Condition
IDEAL: 71%
IDEAL: 100%
IDEAL: 83%
IDEAL: 71%
IDEAL: 64%
IDEAL: 87%
IDEAL: 60%
IDEAL: 67%
Notes: create a balance condition graph to show the idea conditions in green that means we have at enough EML for circadian entrainment under comfortable photopic lux. The red labels here show there is a problematic glare issue especially during the winter when we are looking toward the window. On the other hand, yellow means we have enough photopic light but lacking EML.

## Slide 26
Jun 21st – 12:00pm
Light PNTN: Baseline
Glare - S
S – OPN 1
5500 - 25000 K
S – OPN 1
5500 - 25000 K
S
Glare – E/W
E/W – OPN 1
5500 - 25000 K
E/W – OPN 1
5500 - 25000 K
E/W
N – OPN 1
5500 - 25000 K
Underlit (OPN 4)
N – OPN 1
5500 - 25000 K
N
S: Gaze toward window
E/W: Gaze parallel to window
N: Gaze toward rare wall
Notes: Here is the light penetration analysis on summer solstice: people gaze toward window has a significant glare problem even at 15’ from the window. People gaze parallel to window is slightly better but there is still a glare issue near the window. However, people gaze toward rare wall may experience underlit condition in the central area of the classroom.

## Slide 27
S – OPN 1
5500 - 25000 K
Dec 21st – 12:00pm
Light PNTN: Baseline
S
S – OPN 4
5500 - 25000 K
Glare (S)
E/W – OPN 4
5500 - 25000 K
E/W – OPN 1
5500 - 25000 K
Glare (E/W)
E/W
N – OPN 4
5500 - 25000 K
N – OPN 1
5500 - 25000 K
N
S: Gaze toward window
E/W: Gaze parallel to window
N: Gaze toward rare wall
Notes: On winter solstice: there is a glare problem over the entire classroom. People gaze parallel to window will experience glare issue near the window. People gaze toward rare wall has the best lighting condition

## Slide 28
Baseline (No SF)
Seattle, WA
Climate: Clear
CCT: 5500 – 25000 K
View: East
Dec 21st : 9:00am
Sitting Eye-level: 44”
HDR Imagery
Baseline (No SF)
Seattle, WA
Climate: Clear
CCT: 5500 – 25000 K
View: East
Jun 21st : 9:00am
Sitting Eye-level: 44”
Notes: This is the human visual sensation of the classroom with gaze parallel to window. Similar to the light penetration graph, the classroom appears evenly lit but with potential glare from the window in summer, while the overall light level are lower in winter due to the sun position.
Lighting Conditions: The simulations show significant variations in lighting conditions depending on the time of year, time of day, and correlated color temperature (CCT).
Glare and Brightness: Higher CCT values (25000K) result in circadian brightness levels, especially near windows.
Seasonal Impact: Winter conditions result in generally lower light levels compared to summer, but the relative increase in brightness and glare with higher CCT remains consistent.

## Slide 29
Gray 1% 3% 5% 10%
Location: Seattle, WA
Climate: Clear Sky
CCT: 6500K
Jun 21st : 12:00pm
Sitting Eye-level: 44”
1. Gray (OF: 1% 3%,5%,10%)
Notes: After looking at baseline, we have compare all the openness factor 1%,3%,5%,10%, and here are the results.

## Slide 30
IDEAL: 14%
IDEAL: 14%
IDEAL:8%
IDEAL: 14%
IDEAL: 7%
IDEAL: 8%
IDEAL: 2%
IDEAL: 8%
IDEAL: 14%
IDEAL: 18%
IDEAL: 14%
IDEAL: 18%
IDEAL: 13%
IDEAL: 14%
IDEAL:5%
IDEAL: 14%
IDEAL: 24%
IDEAL: 27%
IDEAL: 14%
IDEAL: 27%
IDEAL: 19%
IDEAL: 20%
IDEAL: 6%
IDEAL: 20%
Balance Conditions : Gray 1% 3% 5% 10%
Summer Jun 21st 12 :00pm
Winter Dec 21st 12 :00pm
IDEAL: 33%
IDEAL: 42%
IDEAL: 18%
IDEAL: 35%
IDEAL: 27%
IDEAL: 31%
IDEAL: 14%
IDEAL: 30%
Notes: Throughout all the openness factor, 10% has better performance which about 1/3 of the area achieve an ideal lighting condition. However, it is also the only option comes with a glare issue for people who gave toward the window during the winter.

## Slide 31
Dec 21st – 12:00pm
Glare (S)
Light PNTN : OF 1% - 10%
S
OPN1
Gray 10%
OPN1
Gray 5%
OPN1
Gray 3%
OPN1
Gray 1%
OPN 4
GRAY 10%
GRAY 5% (OPN4)
OPN 4
GRAY 5%
GRAY 3% (OPN4)
OPN 4
GRAY 3%
GRAY 1% (OPN4)
OPN 4
GRAY 5%
S: Gaze toward window
E/W: Gaze parallel to window
N: Gaze toward rare wall
Notes: Here is the light penetration analysis of those option with gaze toward window. While having a glare issue slightly above the threshold, 10% OF is the only option that doesn’t have circadian underlit problem in all CCT.

## Slide 32
Gray (10%)
Seattle, WA
Climate: Clear
CCT: 5500 - 25000K
View: East
Dec 21st : 9:00am
Sitting Eye-level: 44”
HDR Imagery
Baseline (No Shade)
Seattle, WA
Climate: Clear
CCT: 5500 - 25000K
View: East
Dec 21st : 9:00am
Sitting Eye-level: 44”
Notes: The use of gray (10%) shade fabric is effective in controlling glare and reducing excessive brightness in the classroom environment. It creates a more uniform light distribution, enhancing visual comfort regardless of the season or CCT setting. However, the purple area at the deeper space of the classroom shows a underlit problem which can be resolved by proper manipulation of material based on our photopic and Melanopic sensitivities.

## Slide 33: Finding 1: Commercial typical
If not considering layout, SF with 5% OF would be the safe options in avoiding all glare annually.
With layout planning, SF with 10% OF helps to improve glare control by min. 10% annually.
OF 10% presents a good opportunity for further investigation.
Notes: Here is a small take away. 1, 2, 3.

## Slide 34: Opsin Responsive Color Cube
2. Gray vs Colors (OF: 10%)
B1
B2
B3
G1
G2
G3
R1
R2
R3
Notes: For color exploration, we have remapped a special color cube that uses photopic, Melanopic, and Neuropic responsivity as the XYZ axis. We call this Opsin Responsive Color Cube. This model shows that there’s a variety of colors we can potentially use to retain as much Melanopic responses.

## Slide 35
IDEAL: 33%
IDEAL: 42%
IDEAL: 18%
IDEAL: 35%
IDEAL: 28%
IDEAL: 31%
IDEAL: 14%
IDEAL: 31%
IDEAL: 33%
IDEAL: 57%
IDEAL: 40%
IDEAL: 38%
IDEAL: 28%
IDEAL: 41%
IDEAL: 28%
IDEAL: 34%
OF 10%: Gray/Blue/Purple/Orange
Summer Jun 21st 12 :00pm
Winter Dec 21st 12 :00pm
IDEAL: 36%
IDEAL: 49%
IDEAL: 39%
IDEAL: 40%
IDEAL: 26%
IDEAL: 35%
IDEAL: 26%
IDEAL: 31%
IDEAL: 34%
IDEAL: 25%
IDEAL: 12%
IDEAL: 18%
IDEAL: 27%
IDEAL: 19%
IDEAL: 2%
IDEAL: 19%
Notes: In short, we have tested blue, purple and orange to see how their Melanopic lighting effects. Given OF 10% for all shades, Blue fabric performs better in retaining the Melanopic light as expected. But purple fabric seems to mitigate more glare than blue hence lead to slighting better balance effect.

## Slide 36
S
Jun 21st – 12:00pm
Light PNTN : Colors
OPN 4
Purple 10%
OPN 4
Blue 10%
OPN1
Gray 10%
Blue 10%
Purple 10%
OPN 4
Orange 10%
OPN 4
Gray 10%
OPN 4 Coverage:
Gray (10%) : 31% Blue (10%) : 41%
Purple (10%) : 35% Orange (10%) : 19%
GRAY (OPN4)
Purple (OPN4)
Orange (OPN4)
S: Gaze toward window
E/W: Gaze parallel to window
N: Gaze toward rare wall
Notes: From the plan simulation we can see that blue has improve the overall circadian distribution by 10%, but if we are looking at particular orientation (in this case is gaze toward window), blue color can improve the blue light penetration to the rare wall and eliminate the underlit condition.

## Slide 37
OPN 4 Coverage:
Gray (10%) : 42% Blue (10%) : 57%
Purple (10%) : 49% Orange (10%) : 25%
S
Dec 21st – 12:00pm
Light PNTN : Colors
OPN 4
Blue 10%
OPN 4
Purple 10%
OPN1
Gray 10%
Blue 10%
Purple 10%
Orange 10%
OPN 4
Orange 10%
OPN 4
Gray 10%
Glare (S)
S: Gaze toward window
E/W: Gaze parallel to window
N: Gaze toward rare wall
Orange (OPN4)

## Slide 38
HDR Imagery
Gray (10%)
Blue (10%)
Purple (10%)
Orange (10%)
Seattle, WA
Climate: Clear
CCT: 5500 - 25000K
View: East
Dec 21st : 9:00am
Sitting Eye-level: 44”
Notes: And here are the visual sensations when we deploy the fabrics, the blue fabric also appears to be more align with human visual sensation.
(color constancy: ensures that the perceived color of an object remains relatively constant whether it's observed in sunlight, shade, or artificial light. The brain adjusts the colors based on the light source and surrounding colors, maintaining a stable perception of an object's color despite changes in illumination.)

## Slide 39: Finding 2: Gray vs Color (OF: 10%)
Trans and BRTDfunc files have similar results in grid base simulation, but HDR renders by BRTDfunc is significantly more realistic to human visual sensation.
Manipulate the fabric can improve melanopic light distribution up to 15% in general.
Manipulate the fabric can increase melanopic light penetration over 10’– 0”.
This simulation alters the fabric property via the colors of specular transmission, further investigation would require advanced material science.
Notes: Here are some take way for phase 2

## Slide 40
3. Shade vs Venetian Blinds (VB)
Gray – 50mm spacing, 30° pitch.
Location: Seattle, WA
Climate: Clear Sky
CCT: 6500K
Jun 21st : 12:00pm
Sitting Eye-level: 44”
Notes: Lastly, we are interested in comparing the SF with other fenestration system such as venetian blinds. And just like SF, we have explore a VB in gray and a VB that has different color on both sides (Blue and Red).

## Slide 41
SF (Gray), VB(Gray) , VB(Blue / Red)
Summer Jun 21st 12 :00pm
Winter Dec 21st 12 :00pm
IDEAL: 33%
IDEAL: 42%
IDEAL: 18%
IDEAL: 35%
IDEAL: 27%
IDEAL: 31%
IDEAL: 14%
IDEAL: 30%
IDEAL: 64%
IDEAL: 70%
IDEAL: 43%
IDEAL: 68%
IDEAL: 60%
IDEAL: 62%
IDEAL: 39%
IDEAL: 62%
IDEAL: 65%
IDEAL: 71%
IDEAL: 42%
IDEAL: 69%
IDEAL: 60%
IDEAL: 62%
IDEAL: 40%
IDEAL: 62%
Notes: And here are the results. 1st, VB in general is in general 30% more effect than SF in balancing glare and circadian lighting condition, more effective allowing more light penetration thro the gaps between slabs. But the difference between VB colors is not significant.

## Slide 42
S
Jun 21st – 12:00pm
Light Penetration : Summer
OPN1
SF Gray
SF Blue
OPN 4
SF Gray
OPN 4 Coverage:
SF Gray: 31% VB Gray: 62%
VB Blue: 62% VB Red : 62%
OPN 4
VB Gray
OPN 4
VB Blue / Red
OPN1
VB Gray
VB Blue / Red
OPN 4
SF Blue
S: Gaze toward window
E/W: Gaze parallel to window
N: Gaze toward rare wall
SF Gary
Notes: From the light penetration analysis, we can see that VB help reflect more light into a deeper space with the slabs. However, this feature also makes it not as predictable when comparing with shade fabrics where a sparsity of light distribution is observed.

## Slide 43
OPN 4 Coverage:
SF Gray: 31% VB Gray: 70%
VB Blue: 71% VB Red : 69%
S
Dec 21st – 12:00pm
Light Penetration : Winter
OPN1
SF Gray
SF Blue
OPN 4
Gray 10%
OPN 4
VB Gray
OPN 4
VB Blue / Red
OPN1
VB Gray
VB Blue / Red
S: Gaze toward window
E/W: Gaze parallel to window
N: Gaze toward rare wall
Glare (SF Gray)
Glare (VB)
OPN 4
Blue 10%
Notes: This situation is more obvious during the winter when sun angles are lower and hence have a higher impact to the classroom. In this we have a spike of glare near the center of the classroom which may require further control to resolve. The color variation of blinds show slight improvement (1-2%).

## Slide 44
HDR Imagery
Gray (10%)
Blue (10%)
Purple (10%)
Orange (10%)
Seattle, WA
Climate: Clear
CCT: 5500 - 25000K
View: East
Dec 21st : 9:00am
Sitting Eye-level: 44”
Notes: Here is the visual sensation comparison between SF and VB.

## Slide 45: Conclusions
With current typical products, high OF fabric requires better layout planning to achieve balance:
  If not considering layout, OF 5% would be the safe options for glare prevention.
  With layout planning, OF 10% helps to improve lighting condition by min. 10% annually.
Adjusting the specular transmission can significantly improve the circadian coverage by 10-15%:
  With OF 10%, the color from reflection is less impactful than color from transmission.
  This simulation result invites an opportunity to study material science.
In comparison, venetian blinds is generally 30% more effective in providing the balance:
  It is not as predictable when comparing with shade fabrics.
  The color variation of blinds show slight improvement for about 1-2%.

## Slide 46
Thank You!
“Balancing Glare and Circadian Stimulus with Shade Fabric Simulation”
– Ka Kit Chiu –
B1
B2
B3
G1
G2
G3
R1
R2
R3
Notes: Here is the end of my presentation, thanks again for coming to review my thesis and please feel free to leave any comment.