## Slide 1
Vision Based Surgical Tool Tracking
with Robot Kinematics Prior
Yun-Hsuan Su
Committee: Blake Hannaford, Howard Chizeck
Date: July 31, 2017
Notes: Research topic

## Slide 2
Outline
Introduction
Overview (of the four stages)
Stage 1: Image segmentation
Stage 2: Depth mesh rendering
Conclusion
Future work
Notes: This is the outline of sections we’re covering today

## Slide 3
Introduction
Robot Assisted Minimally Invasive Surgery (MIS)
Collaboration between surgeons and machines.
Advantages:
- High precision beyond human dexterity.
- Remote surgical practices with teleoperation.
1
Notes: Robot assisted minimally invasive surgery (MIS) combines the skill and techniques of highly-trained surgeons with the robustness and precision of machines.
achieved precision is beyond that of human dexterity alone
surgeons are able to operate remotely, i.e. agnostic

## Slide 4
Introduction
Lack of force feedback is a major drawback.
Unintentional tissue damage.
Solution:
(1) Direct force sensing:
Force sensors1 on the surgical tool
Difficulties during sterilization procedures.
2
1. Soo-Chul Lim; Hyung Lee; Joonah Park , 2014, p. 733 – 735, The Institution of Engineering and Technology,Grip force measurement of forceps with fibre Bragg grating sensors
Notes: There is no force feedback in any current commercialized surgical robots.

## Slide 5
Introduction
Lack of force feedback is a major drawback.
Unintentional tissue damage.
Solution:
(1) Direct force sensing:
Force sensors1 on the surgical tool
Difficulties during sterilization procedures.
(2) Vision based force estimation:
Infer force from tissue deformation.
3
1. Soo-Chul Lim; Hyung Lee; Joonah Park , 2014, p. 733 – 735, The Institution of Engineering and Technology,Grip force measurement of forceps with fibre Bragg grating sensors
Notes: Infer the applied force based on real-time analysis of tissue deformation.
This is what my research focuses on

## Slide 6
Overview
Stage 1:
Image segmentation
Stage 2:
Depth mesh rendering
Stage 3:
Force Estimation
Stage 4:
Haptic teleop.
tool
non-tool
raw image
4
Notes: Given a surgical image
Know where the tool is

## Slide 7
Overview
deformation
disparity map
Stage 1:
Image segmentation
Stage 2:
Depth mesh rendering
Stage 3:
Force Estimation
Stage 4:
Haptic teleop.
tool
non-tool
raw image
5

## Slide 8
Overview
deformation
force
disparity map
haptic implementation
Stage 1:
Image segmentation
Stage 2:
Depth mesh rendering
Stage 3:
Force Estimation
Stage 4:
Haptic teleop.
tool
non-tool
raw image
motion
force
6

## Slide 9
Overview
Stage 1:
Image segmentation
Stage 2:
Depth mesh rendering
Stage 3:
Force Estimation
Stage 4:
Haptic teleop.
Master thesis research.
Future work.
7
Notes: Time contraints
After the overview, let jump into each stage

## Slide 10
Stage 1: Image Segmentation
Step 1: Perspective N Points (PNP)
Step 2: Robot Kinematics
Step 3: Color filtering
Step 4: Shape matching with DFT
Step 5: Color mask
Result
Analysis
Stage 1:
Image segmentation
Color filters
Robot
kinematics
Raw image
Segmentation result
8
Real-time
project
Adjust
prediction
3D
2D
Notes: Use this as a prior information
Different sections including steps, result, analysis

## Slide 11
PnP is a method of finding camera extrinsic matrix.
Project surgical tool tip on image.
Step 1: Perspective n Points (PnP)
Stage 1:
Image segmentation
9
Trying to find.
Notes: Suppose we have rotation R and translation t
We can transform the world frame to the camera frame
Compart form
9 eles, 3 eles

## Slide 12
Step 1: Perspective N Points (PNP)
Multiply (1) with
…………………..(3)
Stage 1:
Image segmentation
Unknown extrinsic matrix: ………………..…….(1)
Known intrinsic matrix: ……………..….(2)
known
10

## Slide 13
Step 1: Perspective N Points (PNP)
Stage 1:
Image segmentation
Input:
A set of 3D points and their 2D projections on image.
Output:
The extrinsic matrix
known
input
input
11
Notes: workspace

## Slide 14
Step 2: Robot Kinematics
Raven Surgical Robot System
Open architecture and open source
7 DOF cable-driven robot arm
Stage 1:
Image segmentation
12
Notes: For laparoscopic research
Consists of two

## Slide 15
Step 2: Robot Kinematics
Stick figure from robot kinematics.
Stage 1:
Image segmentation
13
Robot kinematics
Stick figure
Notes: Given the robot kinematics
Tool config  onto image
Static 3D offset

## Slide 16
Step 2: Robot Kinematics
Stick figure from robot kinematics.
Apply 3D static offset.
Stage 1:
Image segmentation
13
Static offset
Stick figure
Stick figure + offset
Notes: Given the robot kinematics
Tool config  onto image
Static 3D offset

## Slide 17
Step 2: Robot Kinematics
Include thickness (width):
Pixel width =
Focal length x Object thickness / Distance to camera.
Stage 1:
Image segmentation
14
Add thickness
Stick figure
Stick figure + offset
Include thickness
Notes: Having stick figure is not enough
Can get a shape prior mask (bottom row)
Tool config + thickness/width

## Slide 18
Step 2: Robot Kinematics
Include thickness (width):
Pixel width =
Focal length x Object thickness / Distance to camera.
Stage 1:
Image segmentation
14
Shape prior U
Predicted projection
Notes: Having stick figure is not enough
Can get a shape prior mask (bottom row)

## Slide 19
Step 3: Color filtering
Robot shape prior mask not perfectly aligned.
Use color filter to examine accuracy of shape prior.
Important color space components2:
Saturation, Hue, Opponent 1, and Opponent 2.
Stage 1:
Image segmentation
15
Shape prior U
Raw image
2. Vision-based and marker-less surgical tool detection and tracking: a review of the literature, David Bouget, Max Allan, Danail Stoyanov, Pierre Jannin, 2016 Elsevier B.V.
Notes: to compensate for the error
Discriminative power

## Slide 20
Step 3: Color filtering
Weighted sum of color space components
Goal: Darker regions --- surgical tool
Brighter regions --- tissue background
Stage 1:
Image segmentation
16
Likelihood Q
weighted sum
Notes: Individual output
Combine everything by the weighted sum of the important components

## Slide 21
Step 4: Shape matching with DFT
Stage 1:
Image segmentation
Likelihood: Q
Q and U may not
perfectly align.
17
Shape prior map: U
Raw image
Robot kinematics
Notes: U from robot kinematics
Q from color filtering
Shift U around so it matches the likelihood the best.
Cost function:
Sum of pixelwise multiplication
Want min(energy map)

## Slide 22
Step 4: Shape matching with DFT
Likelihood map: Q
Shape prior map: U
Stage 1:
Image segmentation
Shape prior U
Likelihood Q
May not perfectly align.
17
Notes: U from robot kinematics
Q from color filtering
Shift U around so it matches the likelihood the best.
Cost function:
Sum of pixelwise multiplication
Want min(energy map)

## Slide 23
Step 4: Shape matching with DFT
Exhaustive search in spatial domain:
Multiplication in frequency domain analogous to convolution in spatial domain3.
Goal: find min value point on the energy map:
Stage 1:
Image segmentation
18
3. Image Segmentation with One Shape Prior – A Template-Based Formulation, Siqi Chena, Daniel Cremersb, Richard J. Radkea, submitted to Image and Vision Computing
Notes: O of N to the 4
O of N square log N

## Slide 24
Step 4: Shape matching with DFT
Stage 1:
Image segmentation
19
energy map
Low energy
(good match)
High energy
Notes: The optimal translational offset is the pixel coordinates of the min value point

## Slide 25
Step 4: Shape matching with DFT
Modify the shape prior U by optimal shifting offset.
Stage 1:
Image segmentation
20
Notes: The vector from image center to the min value point
Is the translational offset

## Slide 26
Step 5: Color mask
Q and U are nicely aligned.
Further improvement: pixel-wise classification
(1) Fine adjust the edges
(2) Deal with partial occlusion.
Stage 1:
Image segmentation
dilate, blur
21

## Slide 27
Step 5: Color mask
Q and U are nicely aligned.
Further improvement: pixel-wise classification
(1) Fine adjust the edges
(2) Deal with partial occlusion.
Stage 1:
Image segmentation
multiply with color mask
22

## Slide 28
Step 5: Color mask
Q and U are nicely aligned.
Further improvement: pixel-wise classification
(1) Fine adjust the edges
(2) Deal with partial occlusion.
Stage 1:
Image segmentation
binary thresholding
23

## Slide 29
Step 5: Color mask
Q and U are nicely aligned.
Further improvement: pixel-wise classification
(1) Fine adjust the edges
(2) Deal with partial occlusion.
Stage 1:
Image segmentation
morphologyEX
24
Notes: Get rid of black spots inside white region
Vice versa

## Slide 30
Result
Stage 1:
Image segmentation
25
Shape prior U
Fourier transform for U and Q
Likelihood Q
Energy map
Tool pose of U and modified U
U and modified U
1. Dilate
2. Color filtering
3. Binary thres.
4. Morphology
Raw image
Segmented tool
Segmented tissue
Notes: A lot of information
Break it down a little bit

## Slide 31
Result
Stage 1:
Image segmentation
25
Shape prior U
Fourier transform for U and Q
Likelihood Q
Energy map
Tool pose of U and modified U
U and modified U
Shape matching with DFT
Notes: We’re going to talk about each of the figures

## Slide 32
Result
Stage 1:
Image segmentation
Shape matching with DFT
Shape prior U
Fourier transform for U and Q
Likelihood Q
25

## Slide 33
Result
Stage 1:
Image segmentation
Shape matching with DFT
Robot kinematics
Color filtering
Shape prior U
Likelihood Q
Fourier transform
Of Shape prior U
Fourier transform
Of Likelihood Q
Shape prior U
Fourier transform for U and Q
Likelihood Q
25
Notes: 4 figures on the bottom left

## Slide 34
Result
Stage 1:
Image segmentation
Raw tool pose
Modified tool pose
U and modified U
Fourier transform of U
Fourier transform of Q
Energy map
Shape matching with DFT
Robot kinematics
Shape matching
with DFT
Tool pose of U and modified U
U and modified U
Energy map
25
Notes: Shape matching
Multiplication of the two fourier transform result

## Slide 35
Result
Stage 1:
Image segmentation
25
1. Dilate
2. Color filtering
3. Binary thres.
4. Morphology
Color mask

## Slide 36
Result
Stage 1:
Image segmentation
1. Dilate
2. Color filtering
3. Binary thres.
Color mask
25

## Slide 37
Result
Stage 1:
Image segmentation
1. Dilate
2. Color filtering
3. Binary thres.
Color mask
1. Dilate and blur the edges
2. Multiplication with color filter
3. Binary thresholding
25

## Slide 38
Result
Stage 1:
Image segmentation
4. Morphology
Color mask
4. Morphology: eliminate black spots
This is also the
surgical tool segmentation mask.

## Slide 39
Result
Stage 1:
Image segmentation
25
Raw image
Segmented tool
Segmented tissue
Segmentation result

## Slide 40
Result
Stage 1:
Image segmentation
25
Raw image
Segmented tool
Segmented tissue
Segmentation result

## Slide 41
Result
Stage 1:
Image segmentation
25
Raw image
Segmented tool
Segmented tissue
Segmentation result
Raw image
Segmented tool
Segmented tissue
(Foreground) (Background)
Notes: This is the result!

## Slide 42
Result
Stage 1:
Image segmentation
26
Displayed speed: x5 times faster (30fps) Original speed: ~ 6fps
Shape matching with DFT
Segmentation result
Color mask
Notes: !!! Right most column Result!!!!
Prediction with offset
Aligned after DFT shape matching
Segmentation result decent.

## Slide 43
Dice Coefficient
Quantify the performance of image segmentation.
The value ranges from 0 to 1
Analysis: Dice coefficient
Stage 1:
Image segmentation
raw image
ground truth
segmentation result
27
Notes: A statistic used for comparing the similarity of two samples.
Suppose |X| and |Y| are the cardinality of the two samples X and Y , the Dice Coeﬃcient is deﬁned as the following:

## Slide 44
Analysis: Dice coefficient
Stage 1:
Image segmentation
Average Dice coefficient value = 0.75
28
raw image
segmented background
segmented tool
segmentation mask
Displayed speed: x5 times faster (30fps) Original speed: ~ 6fps
Notes: Average 0.75
Interested in knowing
if the dice’s coefficient is correlated to tool pose
Recorded a video

## Slide 45
Analysis: Dice coefficient
Stage 1:
Image segmentation
Performance almost uncorrelated with tool pose.
29
Joint 4: tool roll
Joint 5: tool wrist
Joint 6,7: gripper
Dice value
Dice value
Dice value
open
closed
Bent up
Straight down
Front facing
Sideway
Notes: Small correlation.
Good!
Performance independent of tool pose.

## Slide 46
Analysis: Color Statistics
Probability of occurrence for each color in the color space being classified as a tool or non-tool pixel.
Potentially improve color filter.
Stage 1:
Image segmentation
Surgical tool pixels
Tissue pixels
30

## Slide 47
Stage 2: Depth Mesh Rendering
Step 1: Image rectification
Step 2: Disparity correction
Step 3: Disparity post filtering
Step 4: Disparity to depth
Result
Analysis
Stage 2:
Depth mesh rendering
deformation
Disparity map
Segmentation result
Stereo vision
Sphere ROI
Depth map
31
Notes: Again, on the right are sections including the steps result and analysis

## Slide 48
Step 1: Image Rectification
Stage 2:
Depth mesh rendering
Disparity: the apparent pixel diﬀerence or motion between a pair of stereo image.
Prerequisite:
make sure they share a common image plane.
32
Notes: Left and right camera share a common image plane

## Slide 49
Step 1: Image Rectification
Overlay the left and right images on different color channels.
Stage 2:
Depth mesh rendering
After Rectification
Before Rectification
Disparity After Rectification
Disparity
33

## Slide 50
Step 1: Image Rectification
Well rectified image pairs should be row aligned.
Stage 2:
Depth mesh rendering
After Rectification
Before Rectification
Disparity After Rectification
Disparity
34
Notes: As you can see the disparity greatly improved

## Slide 51
Step 2: Disparity correction
Reasonable disparity ≠ Correct disparity
Causes:
(1) Error during camera calibration.
(2) Manufacturing imperfection with the camera.
Correct or not ?
Stage 2:
Depth mesh rendering
35
Notes: Closer brighter
Further darker
Not guanteeed to be correct

## Slide 52
Step 2: Disparity correction
Slight rotation around the y axis
True disparity = Perceived disparity + Shifting offset
Stage 2:
Depth mesh rendering
Parallel case:
Rotated about y case:
36
Notes: Closer brighter
Further darker
Not guanteeed to be correct
Re-projection equations

## Slide 53
Step 2: Disparity correction
Slight rotation around the y axis
True disparity = Perceived disparity + Shifting offset
Stage 2:
Depth mesh rendering
Rotated about y case:
Shifting offset: 46 pixels
37
Notes: Closer brighter
Further darker
Not guanteeed to be correct

## Slide 54
Step 3: Disparity post filtering
Broken points in disparity
Post filtering to reduce the number of broken points.
Stage 2:
Depth mesh rendering
Raw image:
:Disparity
Segmented
Background:
:Segmented Foreground
Region of interest
38

## Slide 55
Step 3: Disparity post filtering
Post filtering schemes:
(1) Max filtering
(2) Weighted least square (wls) filtering4
Stage 2:
Depth mesh rendering
Raw image
Raw Disparity
(by left matching)
Filtered Disparity
(max filtering)
Filtered Disparity
(wls filtering)
39
4. Fast Global Image Smoothing Based on Weighted Least Squares, Dongbo Min, Member, IEEE, Sunghwan Choi, Student Member, IEEE, Jiangbo Lu, Member, IEEE, Bumsub Ham, Member, IEEE, Kwanghoon Sohn, Senior Member, IEEE, and Minh N. Do, Fellow, IEEE, 2013 IEEE

## Slide 56
Step 4: Disparity to depth
Re-project pixel points back into 3D
, where
Stage 2:
Depth mesh rendering
Disparity
+ camera matrices
40
disparity
Notes: Unnormalized 3d points

## Slide 57
Step 4: Disparity to depth
Re-project pixel points back into 3D
Around 1cm re-projection error for the tissue terrain.
Stage 2:
Depth mesh rendering
Raw image
Disparity
2D Pixel points and 3D Re-projections
41
Notes: Into the 3d space

## Slide 58
Result
Stage 2:
Depth mesh rendering
42
Speed: x2.5 times
Notes: A spherical region of interest centered at the tool tip, with 5 cm radius.

## Slide 59
Conclusion
Vision based Surgical Tool Segmentation algorithm with robot kinematics prior.
Using stereo vision, a depth map is generated from the disparity near the tool-tissue interaction point.
Contribution:
  (1) Real time. (~5 fps, no GPU)
  (2) Average Dice coefficient of 0.75
  (3) Image segmentation done on Raven tool instead of Da Vinci tool.
  (4) Adaptable to partial occlusion.
43
Notes: Raven robot system.
Robot kinematics, color filtering
Robust !

## Slide 60
Future work
Stage 1 : Image segmentation
Color statistics to improve the color filter.
Compare dice coefficient without robot kinematics or color filtering.
Stage 2 : Depth mesh rendering
Improve sensitivity down to mm scale.
(Can reduce the baseline of the stereo camera setup.)
Stage 3 : Force Estimation
Stage 4 : Haptic Teleoperation
Implement the next two stages.
Stage 1:
Image segmentation
Stage 2:
Depth mesh rendering
Stage 3:
Force Estimation
Stage 4:
Haptic teleop.
44

## Slide 61
Thank you.
Special thanks to committee members – Blake Hannaford, Howard Chizeck.
And to the wonderful people from the Biorobotics Lab.
45
Notes: all the people I have a chance of meeting

## Slide 62
Questions
Yun-Hsuan Su
Committee: Blake Hannaford, Howard Chizeck
Date: July 31, 2017
46

## Slide 63
Backup slides
Yun-Hsuan Su
Committee: Blake Hannaford, Howard Chizeck
Date: July 31, 2017
Read all

## Slide 64
Lit review
paper 1: feature classification for tracking articulated surgical tools
  (1) 1.2sec/frame
  GPU to enhance efficiency
  (2) CAD model
  (3) Randomized Trees (RT)
  (4) accuracy:
  tool within dashed line
  (93% accuracy)

## Slide 65
Lit review
paper 2: Marker-less Articulated Surgical Tool Detection
  23sec/frame 3sec/frame using pyramid search
  CAD model (on GPU)
  Interesting ideas: vanishing point, tool end in edges
  87% correctness: “on correct tool tip in a visibly consistent joint configuration”

## Slide 66
Lit review
Paper 3: Navigating inner space: 3D assistance for minimally invasive surgery
  30 fps (very fast)
  only tracking with a bounding box, no segmentation
  interesting idea: line recovery

## Slide 67
Step 1: Perspective N Points (PNP)
Stage 1:
Image segmentation

## Slide 68
Step 1: Perspective N Points (PNP)
Stage 1:
Image segmentation
How many points are necessary for pnp computation and why?
6 degrees of freedom, at least 3 points
But if we have more points
We can eliminate worse solutions, and find an optimal

## Slide 69
Step 3: Color filtering
Stage 1:
Image segmentation
Notes: By the weighted sum of the components

## Slide 70
Step 4: Shape matching with DFT
For rotation and scaling.
Stage 1:
Image segmentation

## Slide 71
Step 4: Shape matching with DFT
Proof of concept for shifting using DFT
Stage 1:
Image segmentation

## Slide 72
Step 4: Shape matching with DFT
Proof of concept for rotation and scaling using DFT
Stage 1:
Image segmentation

## Slide 73
Step 4: Shape matching with DFT
Proof of concept for shifting using DFT
Stage 1:
Image segmentation

## Slide 74
Step 4: Shape matching with DFT
Exhaustive search in spatial domain:
Multiplication in frequency domain analogous to convolution in spatial domain3.
Energy map generation:
(1) Exhaustive search in spatial domain:
(2) DFT in frequency domain:
Stage 1:
Image segmentation
18
3. Image Segmentation with One Shape Prior – A Template-Based Formulation, Siqi Chena, Daniel Cremersb, Richard J. Radkea, submitted to Image and Vision Computing
Notes: O of N to the 4
O of N square log N

## Slide 75
Analysis: Dice coefficient
Stage 1:
Image segmentation

## Slide 76
Analysis: Color Statistics
Stage 1:
Image segmentation

## Slide 77
Step 2: Disparity correction
Find out the disparity offset:
Stage 2:
Depth mesh rendering

## Slide 78
Step 2: Disparity correction
Slight rotation around the x axis
Stage 2:
Depth mesh rendering

## Slide 79
Step 2: Disparity correction
Derivation?
Stage 2:
Depth mesh rendering

## Slide 80
Step 2: Disparity correction
Derivation?
Stage 2:
Depth mesh rendering

## Slide 81
Step 3: Disparity post filtering
Broken points (holes) in disparity
(1) discontinuity in depth
(2) thin tool shaft
Stage 2:
Depth mesh rendering

## Slide 82
Step 3: Disparity post filtering
How does weighted least square really works?
Disparity map filter based on Weighted Least Squares filter (in form of Fast Global Smoother that is a lot faster than traditional Weighted Least Squares filter implementations) and optional use of left-right-consistency-based confidence to refine the results in half-occlusions and uniform areas.
http://docs.opencv.org/trunk/d9/d51/classcv_1_1ximgproc_1_1DisparityWLSFilter.html#details
Stage 2:
Depth mesh rendering

## Slide 83
Result
Stage 2:
Depth mesh rendering

## Slide 84
Future work
Improve stereo camera sensitivity down to mm scale.
(Can reduce the baseline.)
why?
if b is smaller, f is fixed.
Increasing the baseline will increase your depth resolution, but will also increase the minimum distance to the camera
Decreasing the baseline will decrease your depth resolution, but will also decrease the minimum distance to the camera
https://nerian.com/support/resources/calculator/
44